## Slide 1: Predictive Maintenance Classifier
Detecting rare machine failures on the UCI AI4I 2020 dataset with a Random Forest and physics-based features
Harsh Paswan · B.Tech Chemical Engineering, BIT Mesra
Python · pandas · scikit-learn · class imbalance · stratified cross-validation

## Slide 2: The problem: failures are rare and costly
UCI AI4I 2020: synthetic milling-machine data, 10,000 production cycles
Inputs: air and process temperature, rotational speed, torque, tool wear, product type
Only 3.39% of cycles fail, so predicting "no failure" every time is 96.6% accurate and catches nothing
Goal: catch real failures (recall) without flooding maintenance with false alarms (precision)
10,000
production cycles
3.4%
failure rate (339 failures)
6
raw sensor features

## Slide 3: Approach: a leakage-safe, imbalance-aware pipeline
1
Clean and encode
Drop UDI and Product ID; encode Type (L/M/H)
2
Prevent leakage
Exclude the failure-mode labels TWF, HDF, PWF, OSF, RNF
3
Stratified split
80/20 with stratify=y keeps the 3.4% ratio in both sets
4
Handle imbalance
Random Forest, 200 trees, class_weight="balanced"
5
Evaluate honestly
Precision, recall, F1, ROC-AUC with 5-fold stratified CV
Accuracy is deliberately not the headline metric: with 3.4% positives it hides every missed failure.

## Slide 4: Baseline: precise, but misses about half of failures
Raw 6 features, single 80/20 split (68 test failures)
Metric | Value
Precision | 0.929
Recall | 0.574
F1 | 0.709
ROC-AUC | 0.969
Confusion matrix (test set)
 | Predicted OK | Predicted fail
Actual OK | 1929 | 3
Actual fail | 29 missed | 39
ROC-AUC is 0.97 but recall is 0.57: the model ranks failures well, yet the default 0.5 cutoff is too strict.
Logistic Regression on the same features reaches F1 of only 0.24: a linear model cannot capture torque × speed interactions.

## Slide 5: Feature engineering from process physics
Power
torque × rotational speed × 2π/60
Captures power failure (PWF)
Temperature difference
process temperature − air temperature
Captures heat dissipation failure (HDF)
Wear × torque
tool wear × torque
Captures overstrain failure (OSF)
Chart: Baseline feature importance
| Torque | Rotational speed | Tool wear | Air temp | Process temp | Type
Importance | 0.338 | 0.277 | 0.209 | 0.099 | 0.063 | 0.014

## Slide 6: Result: recall up 29 points, F1 up 0.23
Chart: 5-fold stratified CV (mean)
| Precision | Recall | F1 | ROC-AUC
Raw 6 features | 0.916 | 0.51 | 0.652 | 0.964
+ Engineered features | 0.979 | 0.797 | 0.878 | 0.973
+29 pts
Recall: 51% → 80%
+0.23
F1: 0.65 → 0.88
98%
Precision (up from 92%)
Threshold 0.5. Recall std across folds: 0.055 → 0.031, so the gain is far larger than the noise.

## Slide 7: Takeaways, limits and next steps
What this shows
Domain-driven features beat extra model complexity
Recall was the right target: a miss means an unplanned breakdown
Cross-validation gave a stable estimate on only 339 failures
Limits and next steps
Random failures (RNF) are unpredictable, capping achievable recall
Synthetic data: validate on real plant data before deployment
Threshold tuning gave only a marginal gain (F1 0.852 → 0.855), so 0.5 is reported
Next: SMOTE comparison, gradient boosting, SHAP explanations
Stack: Python · pandas · NumPy · scikit-learn · matplotlib · seaborn · Jupyter / Colab